## Slide 1
UCL · THE BARTLETT
RESEARCH PLAN · 2026
Waymo Open Sim Agents
Challenge
Task understanding and a research-oriented initial plan
Using WOSAC as a benchmark to study realistic sim-agent design for autonomous driving
Supervisor meeting · 28 April 2026
Notes: Today I want to discuss the Waymo Open Sim Agents Challenge. My goal is not to chase a leaderboard ranking, but to use WOSAC as a standardised benchmark for studying simulation, behaviour modelling and multi-agent interaction in autonomous driving, and to find a focused sim-agent design problem worth optimising.

## Slide 2
Motivation: building research foundations for autonomous driving
WOSAC · Research Plan
01
Why I chose this task
Sim agents sit at the intersection of behaviour modelling, motion prediction, multi-agent interaction, planning evaluation and safety-critical simulation. WOSAC turns these into a single, well-defined benchmark.
1
Behaviour
modelling
2
Motion
prediction
3
Multi-agent
interaction
4
Planning
evaluation
5
Safety-critical
simulation
This project treats the challenge as a research platform — not as a competition submission.
WHAT THE PROJECT WILL DELIVER
01
Reproducible pipeline
WOMD scenarios → Waymax → 32-rollout submission. Three baselines scored against the official meta-metric.
02
Focused sim-agent design
One model targeting a single capability — closed-loop stability, interaction realism, map adherence, or multimodal generation.
03
Failure-mode analysis
Evidence of what the design improves, where it still fails, and how it compares with simple baselines.
Notes: I chose this task because it systematically trains the core capabilities of autonomous driving — prediction, simulation, multi-agent interaction, behaviour modelling, planning evaluation. The aim is not a high leaderboard rank, but to identify a clear modelling problem in this benchmark and improve it in a focused way.

## Slide 3
Background: why realistic simulation matters
WOSAC · Research Plan
02
Real-world testing alone is not enough
expensive to scale
rare or risky scenarios appear infrequently
evaluation feedback is slow and noisy
hard to attribute failures to specific behaviours
Simulation provides a scalable alternative
test rare or risky scenarios at scale
evaluate planning and behaviour models
study multi-agent interactions in closed loop
reduce real-world testing cost
Simulation is useful only if the surrounding agents behave realistically.
The key problem is not replaying logs, but generating realistic interactive traffic behaviour.
Notes: Autonomous-driving systems are hard to evaluate by real-world driving alone — the cost is high, the risk is high, and many edge cases rarely appear. Simulation is therefore essential, but only if the surrounding vehicles, pedestrians and cyclists behave realistically. If they do not, the evaluation of planning and behaviour models is unreliable.

## Slide 4
Task: simulating the future traffic world
WOSAC · Research Plan
03
INPUT — PAST 1 SECOND
Vehicle, pedestrian, cyclist states
Autonomous-vehicle (ADV) state
Road map and lane structure
Traffic-light states
Sim-agent model
OUTPUT — 32 ROLLOUTS × 8 S
Joint future for all agents (incl. ADV)
Each agent: x, y, z position + heading
32 stochastic rollouts per scenario
Example rollout — each box is a simulated agent (position + heading) over 8 s.
The model acts as a traffic-world simulator: it generates how the whole scene evolves, not a single trajectory.
Notes: In plain terms, this task is to train a traffic-world simulator. Given roughly 1 second of real-road history — positions, speeds, pedestrians, cyclists, the road map, traffic lights — the model must generate how the next 8 seconds of the entire scene evolve. Crucially, it does not generate a single future, but 32 possible futures, because the real world is not deterministic. The animation on the right is exactly what a rollout looks like: each box is one simulated agent updating its position and heading every step.

## Slide 5
Framing: from competition task to sim-agent design problem
WOSAC · Research Plan
04
I want to use WOSAC as a controlled benchmark, not as a leaderboard target.
COMPETITION OBJECTIVE
Submit 32 future rollouts per scenario.
fixed format and metric
leaderboard ranking
test-set attempts: 3 per 30 days
MY RESEARCH OBJECTIVE
Identify one modelling weakness and turn it into a strong sim-agent design.
diagnose where baselines fail
isolate one capability to optimise
evaluate what the design improves
WOSAC provides the dataset, simulator, metrics and protocol. My contribution should be a focused model improvement.
Notes: This is the point I want to align on with you: I am not framing this project as 'compete in a challenge'. It already provides data, simulator, submission format and evaluation. So I want to use it as a research platform: pick one specific weakness — closed-loop stability, interaction realism, map adherence — and design a better sim agent around that single point.

## Slide 6
Benchmark platform: data, simulator, submission
WOSAC · Research Plan
05
Dataset — Waymo Open Motion Dataset
Real-world scenarios: agent trajectories, object types, map features, traffic-light states.
Simulator — Waymax
Scenario loading, multi-agent rollout interface, baseline agents, submission generation.
Rollout format
32 rollouts × 8 s (80 steps @ 10 Hz). Position + heading per agent. 150 serialized protos per submission. 3 test-set attempts per 30 days.
Required factorization (2025 rule)
ADV (blue) and world (orange) states must be conditionally independent given the previous joint state. Object dimensions are fixed from the final history frame.
A standardised environment for testing whether a sim-agent design improves realism.
Notes: The benefit of this benchmark is that it is bounded. Data comes from the Waymo Open Motion Dataset; simulation and evaluation can be done in Waymax; the submission is a set of trajectory rollouts, not model code. So it is effectively a standardised experimental environment. The 2025 challenge also requires a specific factorisation: given the previous joint state, the ADV's next state and the world's next state must be conditionally independent — the ego cannot 'peek' at the world's next-step output within the same step. The figure on the right is Waymo's visualisation of that constraint.

## Slide 7
Evaluation: distribution matching, not trajectory error
WOSAC · Research Plan
06
WOSAC scores submissions as a distribution-matching problem: the simulated rollout distribution is compared with the real-world distribution.
Motion realism (kinematic)
linear speed + acceleration
angular speed + acceleration
2025: smoother estimation
Interaction realism
collision (capsule shape — 2025)
distance to nearest object
time-to-collision (vehicles; new filter)
Map adherence
off-road behaviour
distance to road edges
traffic-light violation (2025: NEW)
per-feature negative log-likelihood → weighted-mean meta-metric → higher = more realistic
2025 metric updates mean older leaderboard scores are not directly comparable.
Notes: This is not standard trajectory prediction. The model produces 32 futures, those form a simulated behaviour distribution, and the score asks how well that distribution matches the real-driving distribution. So these metrics also work as diagnostics: they tell me which aspect of the rollout is unrealistic. The 2025 version updated several metrics — capsule-shape collisions, a new traffic-light violation metric, a TTC filter and smoother kinematic estimation — so older baseline numbers are not directly comparable.

## Slide 8
Candidate optimisation points
WOSAC · Research Plan
07
Four directions where baseline sim agents typically fail — the project should pick one.
A
Closed-loop stability
PROBLEM
Small one-step errors accumulate over 80 steps.
POSSIBLE FOCUS
Train a model that stays stable during long autoregressive rollout.
B
Interaction realism
PROBLEM
Independent prediction causes collisions or unrealistic yielding.
POSSIBLE FOCUS
Agent–agent attention or graph-based interaction modelling.
C
Map adherence
PROBLEM
Agents drift off-road or violate lane / traffic constraints.
POSSIBLE FOCUS
Map-conditioned decoding or constraint-aware rollout.
D
Multimodal generation
PROBLEM
One deterministic future cannot represent real-world uncertainty.
POSSIBLE FOCUS
Latent / mixture / token-based sampling for diverse rollouts.
Notes: I do not want to start with one big complex model. The more reasonable path is to run the benchmark, diagnose where baselines fail, then pick the most worthwhile direction — closed-loop stability, interaction realism, map adherence or multimodal generation — so the project's contribution is sharp.

## Slide 9
Proposed initial focus: stable, interaction-aware sim agents
WOSAC · Research Plan
08
A good sim agent must remain stable and socially plausible across an 80-step closed-loop rollout — not just predict the next position accurately.
1
Autoregressive sim-agent model
2
Agent–agent interaction encoding
3
Map-conditioned state update
4
Loss terms: collision · off-road · smoothness
First research goal
Design a sim agent that improves closed-loop realism — not just open-loop prediction accuracy.
Notes: I lean towards starting on closed-loop stability and interaction realism, because the essence of a sim agent is not whether the next step is accurate, but whether 80-step rollouts stay stable, plausible, non-colliding, on-road, and socially realistic between agents.

## Slide 10
Proposed roadmap
WOSAC · Research Plan
09
Diagnosis-driven: understand failures first, then design a focused improvement.
1
Understand data, metrics, rollout format
2
Reproduce Waymax baseline pipeline
3
Diagnose baseline failure modes
4
Select one research focus
5
Design improved sim-agent model
6
Compare against simple baselines
7
Analyse improvements and limitations
PHASE 1
weeks 1–3
Reproduce + diagnose
Stages 1–3
Understand data, run Waymax tutorial, score three baselines, characterise failure modes.
PHASE 2
weeks 4–7
Focused model design
Stages 4–5
Pick one capability, build a sim-agent model around it (encoder, interaction, decoder, losses).
PHASE 3
weeks 8–10
Evaluate + analyse
Stages 6–7
Compare against baselines, analyse where the design improves and where it still fails.
Notes: I do not want to jump straight to a complex model. A safer route is to understand the data and metrics, reproduce the Waymax pipeline, then use simple baselines to expose where the failures are — off-road? collisions? unstable rollouts? Once those are clear, pick one specific direction for the model design.

## Slide 11
Phase 1A · Steps 1–2: understand the data, run the official tutorial
WOSAC · Research Plan
10
1
Understand the data and task format
DATASET — WAYMO OPEN MOTION DATASET v1.2.0
9.1 s scenario @ 10 Hz → ~1.1 s history + 8 s future
Future = 80 simulation steps
Up to 128 agents per scenario; 1 is the AV / ADV
Object types: vehicle · pedestrian · cyclist
Per scenario: trajectories, current state, map, traffic lights
FIRST-WEEK TARGET
Read one scenario and visualise it: past trajectories, lanes, agents, current frame.
2
Run the official Waymax tutorial → first valid submission
THE TUTORIAL HANDLES
Scenario id and Waymax dataloader
Proto format and binary sharding
SimAgentsChallengeSubmission packaging
OUTPUT PER SCENARIO
32 rollouts × 80 steps × all valid agents
(x, y, z, heading) per (agent, step)
Final artefact: 150 protos · .tar.gz · legal submission
Goal of Phase 1A — a working pipeline that produces a legal submission, not a high score.
Notes: Phase 1A has two steps. Step 1 is to understand the data and the task format. WOMD v1.2.0 scenarios are 9.1 seconds at 10 Hz — about 1.1 s history plus 8 s future, which is 80 simulation steps. Each scenario has up to 128 agents with one ADV. The goal here is not to train, just to read and visualise one scenario. Step 2 is to run the official Waymax tutorial end-to-end with a baseline agent like constant-velocity, and produce a legal SimAgentsChallengeSubmission. Score does not matter yet — pipeline correctness does.

## Slide 12
Phase 1B · Steps 3–4: three baselines + first learned model
WOSAC · Research Plan
11
3
Three simple baselines
A
Log replay
Copy the recorded future. Sanity-checks pipeline; invalid for the test set.
B
Constant velocity
Each agent extrapolates current speed in a straight line.
C
Simple interaction rules
Lane-keep + brake on lead car; basic ped/cyclist motion.
Purpose: not to win — to read the metric (e.g. const-vel is fine on motion, fails on off-road / red light).
4
First learned model
INPUT
past 1 s agent states
vector map features
agent type + relative positions
traffic-light state
OUTPUT → next-step Δx, Δy, Δheading
ROLLOUT — REPEAT 80 TIMES
observe simulated scene
predict ADV next state (independent of world per
predict world next state WOSAC factorisation rule)
update scene
By end of Phase 1: working pipeline · 3 baselines scored · 1 learned model trained · failure modes characterised.
Notes: Phase 1B has two steps. Step 3 is to run three simple baselines: log replay (copies the real future, valid only on training/validation), constant velocity, and a simple interaction rule that keeps lane and brakes on lead vehicles. The point is not to win — it is to read the WOSAC metric: which failure modes does each baseline trigger? Step 4 is the first learned model: take a trajectory-prediction model, give it past 1 s agent states, vector map features, agent type, relative positions and traffic-light state, and predict next-step Δx, Δy, Δheading. Train autoregressively; at rollout time loop 80 steps, predicting ADV and world states separately to honour the WOSAC conditional-independence factorisation.

## Slide 13
Phase 2: from single-agent prediction to joint multi-agent simulation
WOSAC · Research Plan
12
The hard part is not predicting one car — it is making all agents jointly plausible.
Agent–agent
interaction
Vehicle ↔ pedestrian
yielding
Car following
Lane keeping
Traffic-light
compliance
Multimodal
futures
Vectorized
map encoder
Agent history
encoder
Agent–agent
attention / GNN
Stochastic
decoder
Constraint-aware
post-processing
autoregressive loop · repeat × 80 steps
Independent per-agent prediction often produces collisions — the agent–agent module exists to fix this.
Success = a clear improvement on one capability with interpretable gains, not a top leaderboard score.
Notes: Phase 2's central insight is that a sim agent is not a one-car predictor — it has to make every agent in the scene jointly plausible. If each agent is decoded independently, two cars will collide, no one will yield, and red lights get ignored. That is why the model recipe puts an agent–agent attention or GNN module between the encoders and the decoder, and why constraint-aware post-processing matters. The WOSAC paper itself states that sim agents must be realistic and interactive — log replay or simple rules are not enough.

## Slide 14
Phase 3: evaluate the design, not only the score
WOSAC · Research Plan
13
Baselines to compare
Constant-velocity
Simple rule-based
Initial learned baseline
Dimensions to analyse
Motion realism
Interaction realism
Map adherence
Closed-loop stability
Diversity across 32 rollouts
Key research question
Which failure mode does the design reduce most clearly?
Does the gain hold across scenario types?
Where does it still fail?
The final result should explain why the model works, where it improves, and where it still fails.
Notes: Evaluation should not be a single aggregate score. The harder question is: what specifically did this design improve? Fewer collisions? Less off-road? More stable 80-step rollouts? More plausible diversity across the 32 rollouts? That kind of analysis is what makes this a research project rather than a contest.

## Slide 15
Discussion questions
WOSAC · Research Plan
14
Q1
Is this a suitable benchmark for building autonomous-driving research foundations?
Q2
Which research focus is most valuable: closed-loop stability, interaction realism, map adherence, or multimodal generation?
Q3
Should I start with rule-based diagnosis or a small learned baseline?
Q4
What would a convincing 4–6 week milestone look like?
Q5
What kind of final output would be most useful — pipeline, model, failure-mode analysis, technical report?
Goal of this meeting — align on scope, focus, and the first milestone.
Notes: What I hope this meeting yields is not a yes/no on 'should I enter the competition'. It is alignment on whether this benchmark is the right research vehicle, and which specific direction to optimise first.

## Slide 16
References
WOSAC · Research Plan
15
1
Montali et al. — The Waymo Open Sim Agents Challenge.
2
Gulino et al. — Waymax: An Accelerated, Data-Driven Simulator for Large-Scale Autonomous Driving Research.
3
Waymo Open Dataset 2025 Sim Agents Challenge — waymo.com/open/challenges/2025/sim-agents/
4
Waymax WOSAC submission tutorial (official GitHub).
5
Waymo Open Dataset Sim Agents tutorial.
6
Recent WOSAC 2024–2025 technical reports.
These are the materials I will read and reproduce; their content is folded into the earlier slides.
Notes: These are the materials I will read and reproduce. The presentation has folded their content into the earlier slides rather than dedicating a slide per paper.